## Slide 1: Electric Potential Difference aka Voltage
Lesson 10

## Slide 2: Electric Potential Difference
Charge does not flow on its own. An electric charge has a certain amount of electrical potential energy because of the electric field set up by the power supply.
Work is done by the power supply to increase the electric potential energy of each coulomb of charge from a low to a high value.
As the charge flows through the load, its energy decreases.

## Slide 3
A load converts electrical energy into another form of energy. You can compare this to the water flowing past a water wheel. The wheel converts some of the energy of the water into motion. The water has more energy before the wheel than after the wheel.

## Slide 4
The electrical potential energy for each coulomb of charge in a circuit is called the electric potential difference (V). Aka Voltage
V
E
Q

## Slide 5
Quantity | Symbol | Units of measurement
Charge | Q | C (coulomb)
Energy | E | J (Joules)
Voltage | V | V (Volts)

## Slide 6
Where E is the energy required to increase the electric potential of a charge, Q. Potential difference is often called voltage.

## Slide 7
The formula can be rearranged
Energy
Charge

## Slide 8
One volt (V) is the electric potential difference between two points if one joule of work (J) is required to move one coulomb (C) of charge between the points.
Joules ∕Coulombs = Volts

## Slide 9: Example 1: potential difference and energy
What is the potential difference across an air conditioner if 72 C of charge transfers 8.5 x 103 J of energy to the fan and compressor?
Q = 72 C
E = 8.5 x 103 J
V = ?

## Slide 11
V = 1.2 x 102 V
Therefore, the potential difference or voltage in the air conditioner is 1.2 x 102 V

## Slide 12: Example 2: Energy and potential difference
A static electric shock delivered to a student from a “friend” transfers 1.5 x 101 J of electric energy through a potential difference of 500 V. What is the quantity charge transferred in the spark?
E = 1.5 x 101 J
V = 500 V
Q = ?

## Slide 14
Q = 0.03 C
Therefore, the charge transfer between friends is 0.03 C.

## Slide 15
Recall that and
So E = VQ and Q = It
Therefore, E = VIt

## Slide 16: Measuring Potential Difference
Potential difference between any two points can be measured using a voltmeter. A voltmeter must be connected in parallel with a load in the circuit in order to compare the potential before and after the load.

## Slide 17: Supplying Electrical Energy
Electrical energy always originates from some other form of energy.
Some common sources include:
Voltaic cells – Chemical potential energy released during a reaction as electrons are driven between two different metals

## Slide 18
Piezo-electricity – Crystals that produce a small electric potential when a mechanical force is placed on them.

## Slide 19
Thermoelectricity – Two different types of metal joined together and subjected to temperature differentials.

## Slide 20
Photo electricity – Light energy absorbed by electrons of certain metals causes charge flow.

## Slide 21
Electromagnetic induction in generators – Kinetic energy forces conductors to rotate in a magnetic field.

## Slide 22: Voltage in Series and parallel Circuits
Kirchhoff’s Voltage Law – The total of all electric potential difference in any complete circuit loop is equal to any potential increases in the circuit loop.
The potential increase, VT is equivalent to the sum of all the potential losses so that
VT = V1 + V2 + V3
V1
V2
V3
VT

## Slide 23
Voltage according to Kirchhoff’s law, this series circuit has one voltage increase of 100V. This voltage must be distributed so that the sum of all voltage drops for each individual resistor must equal this value.
V1
V2
V3
VT

## Slide 24
Find V2
VT = V1 + V2 + V3
So V2 = VT – V1 – V3
V2 = 100 V – 30 V – 30 V
= 40 V
R2
R1
I3
10.0 A
30 V
V2
30 V
100v
10.0 A
10.0 A

## Slide 25: Example 2: Kirchhoff’s laws in a parallel circuit
VT = V1 = V2 = V3
Voltage – The voltage increase is 30 V, thus there must be a decrease for each of the three different parallel resistor paths. Therefore, The voltage drop across all three parallel resistors is 30 V, no matter what their resistances.

## Slide 26
Find V2
VT = V1 = V2 = V3
V2 = 30 V
9.0 A
I3
3.0 A
3.0 A
R3
R2
R1
30V
30V
30V
V2

## Slide 27
Complete lab page 562