## Slide 1: Reducing Electrical Energy Consumption
Lesson 12A

## Slide 2: Units of electrical energy
Energy- The ability to do work
Electrical Energy- The energy transferred to an electrical load by moving charges.
  The symbol for electrical energy is E and the SI unit for measuring energy is called the joule. 1 joule is a very small amount of energy so we use Watt hour and Kilowatt hour.
1 watt hour = 3600 joules.
1 kilowatt hour = 1000 watt hours

## Slide 3: Calculating Electrical Energy
Energy = Power x Time
kWh kW h
Total Energy Used = Speed That Electricity is used x How long electricity is used

## Slide 4: The Cost of Electricity
Every method of generating electricity has an environmental cost. Any time electricity is used in any way; it is using precious resources and costing money.
One way to see how much electricity is used is to look at an electricity meter which tracks how much electricity is drawn from the grid

## Slide 5: The Cost of Electricity
Older models of electricity meters have a dials that show how much electricity has been used. The energy used is calculated monthly or bi-monthly by reading a set of dials above the disk.

## Slide 6: The Cost of Electricity
Newer digital meters, called smart meters, record electricity consumption hour by hour and send the information directly to the utility or electric company.

## Slide 7: The Cost of Electricity
Electricity costs are then calculated according to time of use, which includes time of day, weekdays versus weekends, and season.
  Electricity costs more during peak times, which are the busiest times of the day
  Resources can be saved by reducing your use of electricity at all times of the day.

## Slide 8: Electrical Energy Consumption
The electrical energy consumption for a household is the amount of electrical energy used, usually measured in kilowatt-hours.
A kilowatt-hour (kW•h) is equivalent to the use of one kilowatt in one hour.

## Slide 9: Electrical Energy Consumption
To calculate the cost of using an electrical device, you can multiply the energy consumed in kW•h by the cost per kW•h
Example: the energy (E) used by a microwave oven is 0.8 kW and the oven is turned on for half an hour, the electrical energy used is:
E = 0.8 kW × 0.5 h
= 0.4 kW•h

## Slide 10: Electrical Energy Consumption
One kilowatt (kW) equals 1000 watts (W).
A watt is equal to one joule per second.
If electricity costs 8 cents per kW•h the cost of using the microwave is easily calculated.
Cost = Cost of electricity x kW•h
= 8 cents x 0.4 kW•h
= 3.2 cents.
This may not sound like much but there is also an electricity delivery charge and taxes on top of the actual energy charge.

## Slide 11: Work on the questions and “which light bulb is best?”
Questions
How is a smart meter different from a traditional meter?
Calculate the cost of using each appliance over the course of a year. Use a utility charge of 8.5 cents per kW•h.
Appliance | Average use (hours per day) | Annual Energy Consumption (kW•h) | Annual cost ($ per year)
Vacuum Cleaner | 0.1 | 38 | 
Hair Dryer | 0.25 | 100 | 
Computer | 4.0 | 520 | 
Central air conditioning | 12 (60 days/year) | 1500 | 

## Slide 12: Calculating Percent Efficiency
Lesson 12B

## Slide 13: Calculating Percent Efficiency
An incandescent light bulb uses only about 5 percent of its input energy to create light and converts over 95 percent of its input energy into heat.
Compact fluorescent lights transform about 20 percent of their energy input into light, so they are more efficient than incandescent light bulbs

## Slide 14
The efficiency of a device is the ratio of the useful energy that comes out of the device to the total energy that went in. The more input energy that a device converts into usable output energy, the more efficient the device is.
Efficiency is usually calculated as a percentage.

## Slide 15: Example 1
Suppose a light bulb uses 780 J of input energy to produce 31 J of light energy. What is its percent efficiency?
G | Input energy = 780 J Output energy = 31 J | S | % efficiency = 31 J x 100% 780J = 4.0 %
R | Percent efficiency = ? | P | Therefore, the efficiency of the light bulb is 4.0 percent.
A |  |  | 

## Slide 16: Comparing Efficiency
By comparing the efficiency of different devices, we can judge both their energy cost and their environmental impact.
Read the Label
When buying a new appliance, energy consumption labels help you make an informed choice.
All large appliances such as stoves, dishwashers, refrigerators, washers, and dryers have an EnerGuide label.

## Slide 17: Comparing Efficiency
This label states how much energy that appliance will use in a month or year of average use. (ex 390 kWh)
It also compares the energy consumption of different brands and models. The arrow on the long shaded bar on the label below the rating shows the efficiency range of the appliance

## Slide 18: Comparing Efficiency
If an appliance displays the Energy Star symbol, it is one of the most efficient appliances in its class.

## Slide 19: Comparing Efficiency
In some cesses it is cheaper to buy a newer more efficient appliance than it is to run an old one.

## Slide 20: How Off Is Off?
Most electronics today do not turn completely off. Many are in standby mode which allows them to restart quickly. This means they are using electricity even when they are switched off

## Slide 21: Energy Conservation Begins at Home
You can make a plan to reduce the use of electricity in your home. Asking questions is an excellent start. For example:
Are lights being left on in rooms that are not being used?
Is the clothes dryer being used for small loads like one shirt?

## Slide 22: Energy Conservation Begins at Home
Is the hot water running continuously while the dishes are being done?
Is a lot of hot water being used for long showers?
Are incandescent light bulbs being used instead of compact fluorescent bulbs?

## Slide 23
If we lower our energy demands, we reduce the need to build more generating stations and we avoid greater impact on the environment and major construction costs.
Your own personal action plan to reduce energy consumption will make a difference.
Reusing and recycling materials, conserving energy, and learning to live responsibly in harmony with our environment are key actions for living in a sustainable way.

## Slide 24: Questions
Answer the practice problems
1. A car produces 27.5 kJ of useful output energy from 125 kJ of fuel. What is the car’s percent efficiency?
2. A fluorescent light produces 3.6 kJ of useful light energy from 21 kJ of input energy. What is its percent efficiency?
3. A new high-efficiency brushless motor designed for electric-powered vehicles has an input energy of 75 kJ and an output energy of 72 kJ. What is its percent efficiency?
4. Answer the questions about the community