Lesson plan

Course: 	SNC 2L

Unit: Physics: Using Electrical Energy

Topic: Electricity uses and electromagnets

Lesson: 2

Grade and Level: Grade 10 Locally Developed

Date: 2011

Description of Topic: Today the students will learn about how electricity is converted to different energy forms. The students will then conduct a energy conversion lab.

Learning Expectations

Overall Expectations: PEEV.01 • explain the generation, measurement, and conversion of electricity; PEEV.02 • investigate the factors that affect the generation and use of electricity; PEEV.03 • analyse the social, economic, and/or environmental implications of the sources and uses of electrical energy.

Specific Expectations: PEE1.02 – define and describe electrical concepts (e.g., amps, volts, current, potential difference, energy and power) and their units (e.g., kWh, joules, watts);

| Teacher Resources: Laptop, PP Note, Handout | Student Resources: Handout, Various lab materials |
| --- | --- |

Teaching / Learning Strategies

Note, hands on activity

Steps: (sequence, time lines, teacher/ student roles)

The students will take a note on converting energy The students will complete a lab

Accommodations / Modifications

-The students will have an assisted note where all they have to do is follow along and fill in the blanks. -When it is time for the students to read the article I will try to make time to read it to them. - I will also scribe for students who need a scribe. - The lessons are also posted online so that students can view and listen to the lesson by using programs such as premier.

Assessment & Evaluation

The Students will hand in the lab for evaluation

SNC2L – U3L2										Date:

How do we use Electricity?

In order for electricity to be useful it must be converted into different forms of energy.

Electrical energy is converted into the following:

- Heat

- Light

- Motion

- Sound (really a component of motion)

When energy is converted into any other form of energy some energy is always lost because it is converted into some other form of energy.

Example: a light bulb is made to produce light energy but in the conversion of electrical energy into light energy heat is also produced as a by product. This is what makes the incandescent light bulb so inefficient compared to LED’s.

Electricity to light and heat

Why is heat produced?

Some wires have low resistance

– Electrons pass freely along wire.

Some wires have high resistance

– Electrons pass slowly and “shake.” This causes them to heat up. We see this heat as light.

Electricity to motion

Before we can understand how we can convert electricity to motion we first need to understand how a Permanent magnet works. Magnets have two ends to them. One end is marked North and the other is marked South. Just like the Law of electric charges likes repel and opposites attract. Electromagnets work in the same fashion, except it is temporary. The magnetic field only exists when electric current is flowing through the metal. The magnetic field that is created is the basis of an electromagnet.

| The magnetic field created by a wire is circular. It weakens as the distance from the wire increases. The field is perpendicular to the wire. Since the field is circular we can easily magnify it by coiling the wire. |  |
| --- | --- |

|  | By wrapping the wire around a metal object the magnetic field can be magnified. This will also give the object a distinct North and South end. |
| --- | --- |

How Electric Motors work

|  | An electric motor is all about magnets and magnetism: A motor uses magnets to create motion. So if you have two bar magnets with their ends marked "north" and "south," then the north end of one magnet will attract the south end of the other. On the other hand, the north end of one magnet will repel the north end of the other (and similarly, south will repel south). Inside an electric motor, these attracting and repelling forces create rotational motion. |
| --- | --- |

In the above diagram, you can see two magnets in the motor: The armature (or rotor) is an electromagnet, while the field magnet is a permanent magnet (the field magnet could be an electromagnet as well, but in most small motors it isn't in order to save power).

| You can see that this half-turn of motion is simply due to the way magnets naturally attract and repel one another. The key to an electric motor is to then go one step further so that, at the moment that this half-turn of motion completes, the field of the electromagnet flips. The flip causes the electromagnet to complete another half-turn of motion. You flip the magnetic field just by changing the direction of the electrons flowing in the wire (you do that by flipping the battery over). If the field of the electromagnet were flipped at precisely the right moment at the end of each half-turn of motion, the electric motor would spin freely. |  |
| --- | --- |

Electricity Definitions

| Term | Definition | Symbol |
| --- | --- | --- |
| Energy | Ability to do Work | E |
| Electrical Energy | Energies associated with charges and their movements |  |
| Energy Conversion | Changing one form of energy to another |  |
| Power | Rate energy is transferred . Measured in Watts (W) | P |
| Watt | Unit of power –rate work is done or energy used | W = (J / s) |
| Kilowatt | Unit of power – a measure of electrical work or energy used | kW |
| Joule | A unit of measuring work and energy | J |
| Ampere | Unit of measure for electric current, flow of e- | I |
| Alternating current | Electric current that reverses it’s direction in cycles | AC |
| Direct Current | Electric current that flows in only one direction, Example: battery | DC |
| Circuit | A system of conductors through which electric current flows |  |

SNC2L – U3L2										Date:

How do we use Electricity?

In order for electricity to be useful it must be converted into different forms of energy.

Electrical energy is converted into the following:

- __________(really a component of motion)

When energy is converted into any other form of energy some energy is always lost because it is converted into some other form of energy.

Example: a light bulb is made to produce light energy but in the conversion of electrical energy into light energy heat is also produced as a by product. This is what makes the incandescent light bulb so inefficient compared to LED’s.

Electricity to light and heat

Why is heat produced?

Some wires have low resistance

– _______________________________________

_________________________

– Electrons pass slowly and “shake.” This causes them to heat up. We see this heat as light.

Electricity to motion

Before we can understand how we can convert electricity to motion we first need to understand how a _________________magnet works. Magnets have two ends to them. One end is marked North and the other is marked South. Just like the Law of electric charges likes repel and opposites attract. Electromagnets work in the same fashion, except it is _________________. The magnetic field only exists when electric current is flowing through the metal. The magnetic field that is created is the basis of an electromagnet.

| The magnetic field created by a wire is circular. It weakens as the distance from the wire increases. The field is perpendicular to the wire. Since the field is circular we can easily magnify it by ________________the wire. |  |
| --- | --- |

|  | By wrapping the wire around a metal object the magnetic field can be magnified. This will also give the object a distinct North and South end. |
| --- | --- |

How Electric Motors work

|  | An electric motor is all about magnets and magnetism: A motor uses ___________to create motion. So if you have two bar magnets with their ends marked "north" and "south," then the north end of one magnet will attract the south end of the other. On the other hand, the north end of one magnet will repel the north end of the other (and similarly, south will repel south). Inside an electric motor, these attracting and repelling forces create ___________________________________. |
| --- | --- |

In the above diagram, you can see two magnets in the motor: The armature (or rotor) is an electromagnet, while the field magnet is a permanent magnet (the field magnet could be an electromagnet as well, but in most small motors it isn't in order to save power).

| You can see that this half-turn of motion is simply due to the way magnets naturally attract and repel one another. The key to an electric motor is to then go one step further so that, at the moment that this half-turn of motion completes, the field of the electromagnet __________. The flip causes the electromagnet to complete another half-turn of motion. You flip the magnetic field just by changing the direction of the electrons flowing in the wire (you do that by flipping the battery over). If the field of the electromagnet were flipped at precisely the right moment at the end of each half-turn of motion, the electric motor would spin freely. |  |
| --- | --- |

Electricity Definitions

| Term | Definition | Symbol |
| --- | --- | --- |
|  | Ability to do Work | E |
|  | Energies associated with charges and their movements |  |
|  | Changing one form of energy to another |  |
|  | Rate energy is transferred . Measured in Watts (W) | P |
|  | Unit of power –rate work is done or energy used | W = (J / s) |
|  | Unit of power – a measure of electrical work or energy used | kW |
|  | A unit of measuring work and energy | J |
|  | Unit of measure for electric current, flow of e- | I |
|  | Electric current that reverses it’s direction in cycles | AC |
|  | Electric current that flows in only one direction, Example: battery | DC |
|  | A system of conductors through which electric current flows |  |

SNC2L – U3L2										Date:

Converting Electrical Energy Lab

Converting Electrical energy to light and heat energy

Materials

| Erlenmeyer Flask | 2 Nails | Steel Wool |
| --- | --- | --- |
| Power Source | 2 Wires | Rubber stopper |

Procedure

- Put the nails through the hole in the rubber stopper

- Wrap a very thin piece of steel wool around the bottom of the nails

- Put the stopper in the Erlenmeyer flask

- Attach wires to the top of the nails

- Attach wires to a power source. If nothing happens hook up more batteries

- Turn the power on

Observations C (1)

| Before | During | After |
| --- | --- | --- |

Questions

- What do the results from this test suggest about steel wools resistance to electron flow? T(1)

- How is the energy wasted when it is converted to light? T (1)

Converting Electrical energy to movement

Materials

| Compass | Thin copper wire | Thicker copper wire |
| --- | --- | --- |
| Power Source | magnet | Cardboard, Pencil |

Part 1

| Place a compass on the table. Note the location of north Hook up a battery to a switch and run the wires past the compass. Turn the switch on and watch what happens to the needle. Record your observation in the chart provided Turn the switch off and switch the leads on the battery. Turn the switch back on and note if there is a change in how the needle moved. Record your observation in the chart provided |  |
| --- | --- |

Observations C (2)

| Initial battery orientation | Final battery orientation |
| --- | --- |

Questions

- What caused the needle of the compass to move? T (1)

- Why did the needle of the compass move in a different direction when the direction of current was changed?  T (1)

Part 2

| Procedure 1) Cut piece of cardboard and fold into a “U” 2) Put pencil through cardboard 3) Bend thick copper wire 4) Wrap small copper wires onto each end of thick copper “U” 5) Loop small copper wires over pencil 2 times 6) Large copper “U” should hang like a swing 7) Put magnet under the copper “U” 8) Touch ends of small copper wires to battery | Example |
| --- | --- |

Questions

- What caused the pencil to turn? K (1)

- Is this an efficient means of creating movement? Is heat generated as a well? K (1)

Fill in the electric energy table below

| Item | Power Source | Converts To | Wasted Energy |
| --- | --- | --- | --- |
| Light bulb |  |  |  |
| Electric heater |  |  |  |
| Electric Fan |  |  |  |
| LED light |  |  |  |
| Stove element |  |  |  |
| Speaker |  |  |  |

K (6)

Converting Electrical Energy Rubric

| Criteria | Level 4 | Level 3 | Level 2 | Level 1 |
| --- | --- | --- | --- | --- |
| Thinking Analyzing and interpreting ( / 4) | Draws insightful conclusions based on the data | Draws valid conclusions based on the data | Demonstrates some ability to draw conclusions based on the data | Demonstrates limited ability to draw conclusions based on the data |
| Application Application of lab tools and safety Application of knowledge to new ideas. ( / 5) | Student demonstrates skilful application of lab tools and safety Student applies knowledge to new ideas with a high degree of effectiveness | Student demonstrates sufficient application of lab tools and safety Student applies knowledge to new ideas with considerable effectiveness | Student demonstrates limited application of lab tools and safety Student applies knowledge to new ideas with moderate effectiveness | Student demonstrates very limited application of lab tools and safety Student applies knowledge to new ideas with limited effectiveness |
| Communication Communication of information and ideas ( /3) | Communicates information and ideas clearly and precisely | Communicates information and ideas with considerable clarity and precision | Communicates information and ideas with some clarity and precision | Communicates information and ideas with limited clarity and precision |
| Knowledge Knowledge of electricity and electromagnetism ( /7) | Student has superior knowledge of electricity and electromagnetism | Student has sufficient knowledge of electricity and electromagnetism | Student has limited knowledge of electricity and electromagnetism | Student has very limited knowledge of electricity and electromagnetism |